ALICE Electronic Rack Layout

(“Location and Allocation”)

J.P. Vanuxem, C.H. Denarié, PH-AIS

Andre Augustinus PH-AIT

# Abstract

This document defines the position of some 300 electronic racks in ALICE, and their allocation to various sub-detectors or sub-systems.

# Table of Contents

Abstract	1

Table of Contents	2

Figures and Tables	2

1. Introduction	3

2.1 Racks in UX25 cavern	5

2.1.1 Group ‘I’	6

2.1.2 Group ‘O’	7

2.1.3 Group ‘A’	8

2.1.4 Group ‘C’	9

2.2 Racks in PX24 Counting rooms	10

2.2.1 Level 1	11

2.2.2 Level 2	12

2.2.3 Level 3	13

2.2.4 Level 4	14

2.2.5 Level 5	15

2.3 Miscellaneous Racks	16

Appendix 1:  List of Coordinators and Contact Persons	20

Appendix 2:  Rack Allocation Detailed Listing	21

# Figures and Tables

Figure 1: Basic underground structures at Point 2	3

Figure 2: Layout of racks in Point 2 experimental area	4

Figure 3: The four groups of racks in UX25	5

Figure 4: Rack layout, group I	6

Figure 5: Rack layout, group O	7

Figure 6: Rack layout, group A	8

Figure 7: Rack layout, group C	9

Figure 8: Typical 3-row rack arrangement in the 4 counting rooms	10

Figure 9: Rack layout in CR1	11

Figure 10: Rack layout in CR2	12

Figure 11: Rack layout in CR3	13

Figure 12: Rack layout in CR4	14

Figure 13: Rack layout on CR5	15

Figure 14:  Typical internal rack arrangement: a TPC-LV rack (in group A)	19

Table 1: Rack allocation, group I	6

Table 2: Rack allocation, group O	7

Table 3: Rack allocation, group A	8

Table 4: Rack allocation, group C	9

Table 5: Rack allocation in CR1	11

Table 6: Rack allocation in CR2	12

Table 7: Rack allocation in CR3	13

Table 8: Rack allocation in CR4	14

Table 9: Rack allocation on CR5	15

Table 10:  Rack Allocation in ACR	16

Table 11:  Rack Allocation in MCR	16

Table 12:  Rack Allocation in US25	16

Table 13: Number of electronic racks per type in ALICE	18

# 1. Introduction

This document defines a total of 299 electronic rack locations inside the ALICE surface and underground structures, of which 264 will be equipped: 222 racks allocated to sub-detectors and sub-systems, 27 integration racks and 15 minimally-equipped (just power and cooling water) spare racks. The other (either empty, or occupied but unequipped) 35 rack locations are reserved for possible future extension(s). Most figures in this document are based on drawings made by S. Maridor, C. Fillion-Robin, D. Gabriele and E. Sabin.

About half the total number of rack locations (137 exactly) are physically split into 4 groups in the UX25 experimental cavern and will mostly contain LV power supplies, sub-detector readout systems and DCS equipment. The other ‘half’ (152 exactly) are situated in the 4 counting rooms CR1 to CR4 and on the CR5 plug of the PX24 access shaft and will mostly contain PC farms for the DAQ, HLT and DCS sub-systems in CR1, CR2 and CR3 respectively, miscellaneous equipment (mostly HV power supplies) in CR4 and mostly security systems equipment on the CR5 plug. Finally, 2 rack locations are defined in the ALICE Control Room (ACR) of the SX2 surface building, 3 in the US25 service area and 5 in the Magnet Control Room (MCR) close to CR4 and on the same level 4 of PX24.

Owing to cost reasons, and with the exception of the 15 minimally-equipped spare racks, only locations which have been allocated to sub-detectors or sub-systems will be filled with equipped racks. However, the power distribution, its control and monitoring and the rack water cooling systems will be originally designed for the full number of locations, such that later eventual additional installation(s) of racks (up to the maximum number of locations available) will be easy. Fig. 1 shows the general layout of the ALICE Experiment, with its surface building SX2, underground experimental area UX25 and access shaft PX24 in between.

Figure 1: Basic underground structures at Point 2

2. Rack Layout

Most of the electronic racks are installed in the UX25 experimental cavern and in the PX24 shaft (Fig.2). The racks in UX25 are not accessible during machine operation and are installed in an open configuration. The four counting rooms CR1-CR4 in PX24 provide a closed environment whilst the shielding plug, being situated at level 5 of PX24, will be named ‘CR5’ by extension and for convenience, although it has no roof and no protecting walls. CR1-CR5 are accessible at all times.

Figure 2: Layout of racks in Point 2 experimental area

The fixed part of the shielding plug separating the public area from the radiation-controlled cavern, also serves as a convenient platform for gas distribution racks. All services enter the experimental area via two chicane arrangements incorporated at the circumference of the shielding plug. The UX25 cavern has a system of fixed cable trays covering the entire length of the cavern and the part of the PX24 access shaft below the shielding plug.

## 2.1 Racks in UX25 cavern

A total of 137 electronic rack locations are defined in the UX25 experimental cavern. These rack locations are split in 4 groups, as shown by Fig. 3 : 38 locations on gallery ‘I’ besides the L3 magnet along the cavern wall and looking ‘Inside’ the LHC machine (as seen from the beam intersection point); 37 locations on gallery ‘O’ besides the L3 magnet  along the cavern wall and looking ‘Outside’ the LHC machine; 22 locations under the beam line shielding on the RB24 side (group A); 40 locations under the muon platform on the RB26 side (group C). Each rack allocated in UX25 has a unique label and sub-detector assignment, and is of the LHC standard type, 1000 mm deep, and either 41 U high (LHC-41) wherever vertical space is limited (namely in the most part of the two side galleries I and O and also in the central region of group C), or 52 U high (LHC-52) elsewhere.

Figure 3: The four groups of racks in UX25

### 2.1.1 Group ‘I’

38 rack locations are defined on the upper side-platform (Fig. 4) looking towards the Inside of the LHC machine. The rack allocation in group I is shown on Table 1.

Figure 4: Rack layout, group I

Table 1: Rack allocation, group I

| Function | Number of Racks | Rack Type | Rack Position |
| --- | --- | --- | --- |
| HMP (TR,LV) | 3 | LHC-41 | I00-I02 |
| TOF (LV) | 6 | LHC-41 | I03-I05, I30-I32 |
| TRD (LV) | 5 | LHC-41 | I06,I26-I29 |
| TRD (CO, HV) | 2 | LHC-41 | I07-I08 |
| TS-EL | 2 | LHC-41 | I16-I17 |
| SPD (LV) | 2 | LHC-41 | I18-I19 |
| V0 (RO) | 1 | LHC-41 | I20 |
| SSD (RO, LV/HV, CO) | 4 | LHC-41 | I21-I24 |
| TPC (LV) | 1 | LHC-41 | I25 |
| TOF (spare) | 1 | LHC-41 | I33 |
| MTR (RO) | 4 | LHC-52 | I34-I37 |
| Equipped racks | 31 | 4 LHC-52 + 27 LHC-41 |  |
| Spare rack locations | 7 | LHC-41 | I09-I15 |
| Total | 38 | 4 LHC-52 + 34 LHC-41 |  |

### 2.1.2 Group ‘O’

37 locations are defined for electronic racks on the upper side-platform (Fig. 5) looking towards the Outside of the LHC machine, one additional location (O17) being reserved for TPC gas distribution. The rack allocation in group O is shown on Table 2.

Figure 5: Rack layout, group O

Table 2: Rack allocation, group O

| Function | Number of Racks | Rack Type | Rack Position |
| --- | --- | --- | --- |
| TOF (spare) | 2 | LHC-41 | O02, O33 |
| TOF (LV) | 6 | LHC-41 | O03-O05, O30-O32 |
| TRD (LV) | 5 | LHC-41 | O06, O26-O29 |
| TRD (CO, HV) | 2 | LHC-41 | O07-O08 |
| EMC (LV) | 1 | LHC-41 | O12 |
| FMD (LV) | 1 | LHC-41 | O13 |
| ACO (LV, RO) | 2 | LHC-41 | O14-O15 |
| TS-EL | 1 | LHC-41 | O16 |
| (TPC-GAS) | (1) | (Special gas rack) | (O17) |
| T0 (LV, RO) | 2 | LHC-41 | O18-O19 |
| SDD (LV) | 1 | LHC-41 | O20 |
| Sniffer Detection | 2 | LHC-41 | O21-O22 |
| Sniffer Detection (spare) | 1 | LHC-41 | O23 |
| Min-equipped spare rack | 1 | LHC-41 | O24 |
| TPC (LV) | 1 | LHC-41 | O25 |
| MTR (RO) | 4 | LHC-52 | O34-O37 |
| Equipped racks (electronic racks only) | 32 | 4 LHC-52 + 28 LHC-41 |  |
| Unequipped spare rack | 1 | LHC-41 | O11 |
| Spare rack locations (electronic racks only) | 4 | LHC-41 | O00-O01, O09-O10 |
| Total (electronic racks only) | 37 | 4 LHC-52 + 33 LHC-41 |  |

### 2.1.3 Group ‘A’

22 rack locations are defined under the beam shielding (Fig. 6) on the RB24 side. The rack allocation in group A is shown on Table 3.

Figure 6: Rack layout, group A

Table 3: Rack allocation, group A

| Function | Number of Racks | Rack Type | Rack Position |
| --- | --- | --- | --- |
| Vacuum | 1 | LHC-52 | A03 |
| TPC (LV) | 2 | LHC-52 | A04-A05 |
| TPC (Pulser) | 2 | LHC-52 | A06-A07 |
| PMD (LV) | 2 | LHC-52 | A08-A09 |
| SDD (LV) | 1 | LHC-52 | A12 |
| Min-equipped spare rack | 1 | LHC-52 | A13 |
| SPD (LV) | 2 | LHC-52 | A14-A15 |
| CPV (LV) | 1 | LHC-52 | A16 |
| PHS (LV) | 1 | LHC-52 | A17 |
| TS-EL | 1 | LHC-52 | A18 |
| SSD (RO, LV/HV) | 3 | LHC-52 | A19-A21 |
| Equipped racks | 17 | LHC-52 |  |
| Spare rack locations | 5 | LHC-52 | A00-A02, A10-A11 |
| Total | 22 | LHC-52 |  |

### 2.1.4 Group ‘C’

40 electronic rack locations are defined under the muon platform (Fig. 7) on the RB26 side. The rack allocation in group C is shown on Table 4.

Figure 7: Rack layout, group C

Table 4: Rack allocation, group C

| Function | Number of Racks | Rack Type | Rack Position |
| --- | --- | --- | --- |
| TS-EL | 1 | LHC-52 | C00 |
| MTR (LV) | 2 | LHC-52 | C01, C31 |
| TOF (RO, TR) | 2 | LHC-52 | C02-C03 |
| SPD (TR) | 1 | LHC-52 | C04 |
| MCH (LV) | 10 | LHC-52 | C05, C08-C11, C32, C36-C39 |
| Min-equipped spare rack | 2 | LHC-52 | C12-C13 |
| TPC (Pulser) | 2 | LHC-52 | C14-C15 |
| TRD (RO, TR) | 3 | 1 LHC-41 + 2 LHC-52 | C16-C18 |
| TRI (CTP) | 6 | LHC-41 | C20-C21, C24-C27 |
| Multiple Trigger (MCH,MTR,SPD,PMD) | 2 | LHC-41 | C22-C23 |
| BIC (Beam Interlock Controller) | 2 | LHC-52 | C28-C29 |
| Vacuum | 1 | LHC-52 | C30 |
| Equipped racks | 34 | 25 LHC-52 + 9 LHC-41 |  |
| Unequipped spare rack | 1 | LHC-52 | C19 |
| Spare rack locations | 5 | LHC-52 | C06-C07, C33-C35 |
| Total | 40 | 31 LHC-52 + 9 LHC-41 |  |

## 2.2 Racks in PX24 Counting rooms

A total of 152 electronic rack locations are defined in the four counting rooms CR1-CR4 and on the plug platform CR5 of the PX24 access shaft.

The counting room closest to the surface is labeled CR1; the three counting rooms below are labeled CR2, CR3 and CR4 respectively. The different levels can be reached by a dedicated lift installation and two independent staircases. The false floor of each level is directly connected to a vertical service shaft, which permits easy access for installation of cables. Each counting room has a surface of 80 m2 and is equipped with air cooling (for ambient temperature) of 50 kW cooling capacity and water cooling (for racks) of 350 kW cooling capacity. Most of the existing installations (racks and cabling) will be kept as they were in CR1, CR3 and CR4, while CR2 and CR5 will need a new installation.

Each rack allocated in PX24 has a unique label and sub-detector assignment. It is of the plain LEP type (LEP-56) in CR4 and CR5, and mostly of the modified LEP type (LEP-56PC) in CR1-CR3 allowing for horizontal air ventilation as required by PC farms.

Fig. 8 shows a typical 3-row rack arrangement in the four counting rooms (case of CR1). In this example, the EXD 1/20 switchboard (a ‘double Hazemeyer’ unit) provides 3-phase 400V electric power to 35 racks. As it only contains 22 contactors / circuit breakers/ feeder modules, one such module is used for 2 racks.

Figure 8: Typical 3-row rack arrangement in the 4 counting rooms

### 2.2.1 Level 1

CR1, except for one rack reserved for power distribution control (TS-EL), is used exclusively for DAQ equipment (computers, network, and storage). There are 35 rack locations in CR1 (Fig. 9), which are allocated as shown in Table 5.

Figure 9: Rack layout in CR1

Table 5: Rack allocation in CR1

| Function | Number of Racks | Rack Type | Rack Position |
| --- | --- | --- | --- |
| TS-EL | 1 | LEP-56 | X01 |
| DAQ-LDCs (HLT) | 1 | LEP-56PC | X02 |
| DAQ-LDCs (MCH, MTR) | 1 | LEP-56PC | X03 |
| DAQ-LDCs (PHOS-CPV) | 1 | LEP-56PC | X04 |
| DAQ-LDCs (HMPID-PMD) | 1 | LEP-56PC | X05 |
| DAQ-LDCs (TOF) | 2 | LEP-56PC | X06-X07 |
| DAQ-LDCs (TRD) | 1 | LEP-56PC | X08 |
| DAQ-LDCs (SSD-FMD) | 1 | LEP-56PC | X09 |
| DAQ-LDCs (SDD-ZDC-ACORDE) | 1 | LEP-56PC | X10 |
| DAQ-LDCs (SPD) | 1 | LEP-56PC | X11 |
| DAQ-LDCs (TPC) | 12 | LEP-56PC | Y01-Y12 |
| DAQ-LDCs (EMC) | 1 | LEP-56PC | Y13 |
| DAQ-CO (Test & Comm.) | 1 | LEP-56PC | Z01 |
| DAQ-CO (Servers) | 1 | LEP-56PC | Z02 |
| DAQ-GDCs | 5 | LEP-56PC | Z03-Z04, Z06-Z08 |
| DAQ-CO (EB SW & KVM) | 1 | LEP-56PC | Z05 |
| Equipped spare racks for DAQ | 3 | LEP-56PC | Y14, Z09-Z10 |
| Total equipped racks | 35 | 1 LEP-56 + 34 LEP-56PC |  |
| Spare rack locations | 0 |  |  |
| Total | 35 | 1 LEP-56 + 34 LEP-56PC |  |

### 2.2.2 Level 2

CR2, except for one rack reserved for power distribution control (TS-EL), is used exclusively for HLT equipment (computers, network, and storage). There are 40 rack locations in CR2 (Fig. 10), which are allocated as shown in Table 6.

Figure 10: Rack layout in CR2

Table 6: Rack allocation in CR2

| Function | Number of Racks | Rack Type | Rack Position |
| --- | --- | --- | --- |
| TS-EL | 1 | LEP-56 | X01 |
| HLT-CO (Network, Switch and Monitoring) | 3 | LEP-56PC | X02, Y01, Z01 |
| HLT-PC (Computing Nodes) | 36 | LEP-56PC | X03-X10, Y02-Y17, Z02-Z13 |
| Total equipped racks | 40 | 1 LEP-56 + 39 LEP-56PC |  |
| Spare rack locations | 0 |  |  |
| Total | 40 | 1 LEP-56 + 39 LEP-56PC |  |

### 2.2.3 Level 3

CR3 is mostly used for DCS and HLT equipment (computers, network, and storage). Three racks are also used for TOF control, and one rack is reserved for power distribution control (TS-EL). There are 35 rack locations in CR3 (Fig. 11), which are allocated as shown in Table 7.

Figure 11: Rack layout in CR3

Table 7: Rack allocation in CR3

| Function | Number of Racks | Rack Type | Rack Position |
| --- | --- | --- | --- |
| HLT-PC (Computing Nodes) | 12 | LEP-56PC | X01-X12 |
| TS-EL | 1 | LEP-56 | Y01 |
| TOF-CO | 3 | LEP-56PC | Y02-Y04 |
| DCS-DC (ITS, FMD) | 1 | LEP-56PC | Z01 |
| DCS-DC (TPC,HMP,PMD) | 1 | LEP-56PC | Z02 |
| DCS-DC (TRD,V0,T0) | 1 | LEP-56PC | Z03 |
| DCS-DC (PHS,CPV,EMC,ZDC,ACO) | 1 | LEP-56PC | Z04 |
| DCS-CO (MCH,MTR,TOF) | 1 | LEP-56PC | Z05 |
| DCS TRG,SPD TRG, DCS | 1 | LEP-56PC | Z06 |
| DCS Central DCS | 1 | LEP-56PC | Z07 |
| DCS-CO (Fieldbusses) | 1 | LEP-56 | Z08 |
| Min-equipped spare racks | 4 | LEP-56 | Y05-Y08 |
| Total equipped racks | 28 | 6 LEP-56 + 22 LEP-56PC |  |
| Unequipped spare racks | 7 | LEP-56 | Y09-Y13, Z09-Z10 |
| Total | 35 | 2 LEP-56 + 33 LEP-56PC |  |

### 2.2.4 Level 4

CR4 houses mostly HV power supplies for various detectors, but also miscellaneous electronic equipment for MCH-GMS (Geometry Monitoring System), DSS (Detector Security System) and ZDC (Zero Degree Calorimeter). As for the 3 previously described counting rooms CR1-CR3, one rack is reserved for power distribution control (TS-EL). There are 34 rack locations in CR4 (Fig. 12), which are allocated as shown in Table 8.

Figure 12: Rack layout in CR4

Table 8: Rack allocation in CR4

| Function | Number of Racks | Rack Type | Rack Position |
| --- | --- | --- | --- |
| MCH (GMS) | 1 | LEP-56 | X01 |
| ACO (HV) | 1 | LEP-56 | X02 |
| PMD (HV) | 1 | LEP-56 | X03 |
| ZDC (RO) | 2 | LEP-56 | X04-X05 |
| FMD (HV) | 1 | LEP-56 | X06 |
| SPD (RO,HV) | 3 | LEP-56 | Y01-Y03 |
| SDD (HV,RO) | 2 | LEP-56 | Y04-Y05 |
| SSD (HV) | 1 | LEP-56 | Y06 |
| TPC (HV,VHV) | 2 | LEP-56 | Y08, Z08 |
| PHS/CPV/EMC (HV) | 1 | LEP-56 | Y10 |
| HMP (HV) | 1 | LEP-56 | Y11 |
| TRD (HV, spare) | 2 | LEP-56 | Y12-Y13 |
| TS-EL | 1 | LEP-56 | Z01 |
| TOF (HV) | 2 | LEP-56 | Z02-Z03 |
| T0/V0 (HV) | 1 | LEP-56 | Z04 |
| MCH (HV) | 1 | LEP-56 | Z05 |
| MTR (HV) | 1 | LEP-56 | Z06 |
| DCS-DSS | 1 | LEP-56 | Z09 |
| Min-equipped spare racks | 7 | LEP-56 | X07-X09, Y07, Y09, Y14, Z07 |
| Total equipped racks | 32 | LEP-56 |  |
| Unequipped spare racks | 2 | LEP-56 | X10-X11 |
| Total | 34 | LEP-56 |  |

### 2.2.5 Level 5

CR5 is the shielding plug platform. It contains primarily gas distribution racks for the sub-detectors. There are however 8 electronic rack locations on CR5 (Fig. 13) which are essentially foreseen for Safety Systems and HMPID liquid circulation control. These locations are allocated as shown in Table 9.

Figure 13: Rack layout on CR5

Table 9: Rack allocation on CR5

| Function | Number of Racks | Rack Type | Rack Position |
| --- | --- | --- | --- |
| Sniffer Control | 1 | LEP-56 | X01 |
| Fire Detection (racks) | 2 | LEP-56 | X02-X03 |
| Fire Detection (detector) | 1 | LEP-56 | X04 |
| Radio-protection | 1 | LEP-56 | X05 |
| Equipped spare rack for Safety | 1 | LEP-56 | X06 |
| HMP (CO) | 2 | LEP-56 | X07-X08 |
| Total equipped racks | 8 | LEP-56 | X01-X08 |
| Spare rack locations | 0 |  |  |
| Total | 8 | LEP-56 | X01-X08 |

## 2.3 Miscellaneous Racks

Other rack locations are defined in ALICE in three miscellaneous areas:

2.3.1 ACR

The ALICE Control Room (ACR) in SX2 will need control and monitoring equipment for DCS (DSS) and Trigger (Monitoring). There are 2 electronic rack locations in a small room next to ACR, which are allocated as shown in Table 10.

Table 10:  Rack Allocation in ACR

| Function | Number of Racks | Rack Type | Rack Position |
| --- | --- | --- | --- |
| DCS-DSS | 1 | LEP-56 | SX2-X01 |
| TRI | 1 | LEP-56 | SX2-X02 |
| Total equipped racks | 2 | LEP-56 | SX2-(X01-X02) |
| Spare rack locations | 0 |  |  |
| Total | 2 | LEP-56 | SX2-(X01-X02) |

2.3.2 MCR

The Magnet Control Room (MCR) at level 4 of PX24 contains equipment for the control and monitoring of the two ALICE magnets: the L3 magnet and the Dipole. There are 5 electronic rack locations in MCR, which are allocated as shown in Table 11.

Table 11:  Rack Allocation in MCR

| Function | Number of Racks | Rack Type | Rack Position |
| --- | --- | --- | --- |
| Magnets Control (L3 and Dipole) | 5 | LEP-56 | CR4-(M01-M05) |
| Total equipped racks | 5 | LEP-56 | CR4-(M01-M05) |
| Spare rack locations | 0 |  |  |
| Total | 5 | LEP-56 | CR4-(M01-M05) |

2.3.3 US25

This area is not strictly speaking part of the ALICE experiment. However, in order to be complete, there are 3 electronic rack locations for ALICE in US25, which have not been allocated yet, as shown in Table 12.

Table 12:  Rack Allocation in US25

| Function | Number of Racks | Rack Type | Rack Position |
| --- | --- | --- | --- |
| Equipped racks | 0 |  |  |
| Unequipped racks | 3 | LEP-56 | US2-(X01-X03) |
| Total | 3 | LEP-56 | US2-(X01-X03) |

3. Rack types

Most electronic equipment in ALICE is mounted in standard 19” racks. The five counting rooms CR1-CR5 in PX24, the ALICE Control Room (ACR) in SX2, the Magnet Control Room (MCR) in PX24 and the US25 area are equipped with LEP type racks (i.e. racks previously used by either L3 or ALEPH experiment): they are 56 U high and 900 mm deep (LEP-56). In UX25, all racks are of the type recommended as rack standard for LHC experiments: 1000 mm deep and 41 U high (LHC-41) wherever vertical space is restricted, i.e. in most of the two side galleries I and O and in the central region of group C, and 52 U high (LHC-52) elsewhere.

However, racks in CR1, CR2 and CR3 containing rack-mounted PC equipment will be equipped with a special, horizontal air ventilation system. In these racks (LEP-56PC), the cooling is realized by a cold water column placed in the back of the rack.

There will thus be four different rack types in ALICE: LEP-56 and LEP-56PC are LEP types, the latter allowing for horizontal air flow as required by PCs; LHC-52 and LHC-41 are LHC types, respectively 52 U and 41 U high. Table 13 is a summary of the use of these four rack types in ALICE: the first number indicated is the number of electronic racks already allocated (i.e. ‘to be equipped’), the second is the number of additional spare rack locations (occupied or not by an unequipped rack) available for eventual future expansion.

Each electronic rack is powered from an electrical distribution rack (a “Hazemeyer unit”, named “EXD” (for standard power) or “EOD” (for UPS power) in the rack layout figures previously shown). The Hazemeyer units contain contactors / circuit breakers in their 3-phase ‘ZTBX32 drawers’ power modules. Due to the limited number of such modules available, one module will feed 2 racks in the 4 counting rooms CR1-CR4 of PX24 instead of the usual one rack elsewhere for standard power. The standard maximum rating of the circuit breakers is 32 A (except for 9 ‘superpower racks’, where it is 63 A) on all three phases, which allows for a maximum power of 7 kW per phase. The general power distribution is however limited in size by an average of 8 kW per rack (total for all 3 phases) within either a group (in UX25) or a counting room (in PX24). The power for electronic racks, both in UX25 and PX24, comes from dedicated transformers, different from those feeding the 2 magnets and the general services, in order to isolate them from  potential sources of electrical noise.

204 out of the 299 available rack locations in ALICE are planned to house modular electronics mounted in crates and to be cooled by standard vertical air ventilation. Heat exchangers, in the form of horizontal radiators, are placed in the vertical air flow in order to remove the heat via the water cooling system. A typical internal rack arrangement is shown on Fig. 14, with some LV power supply equipment for the TPC in the example. Note that, due to their incompatibility with magnetic fields higher than 80 Gauss, the use of 1U horizontal fan units in ALICE should in principle be avoided in the C area of the UX25 cavern.

|  | Group# / CR# | LHC-41 | LHC-52 | LEP-56 | LEP-56PC | All types |
| --- | --- | --- | --- | --- | --- | --- |
| Rack Height (U) |  | 46 | 52 | 56 | 56 |  |
| Rack Depth (mm) |  | 1000 | 1000 | 900 | 900 |  |
| UX25 | I | 27+7 | 4+0 |  |  | 31+7 |
| UX25 | O | 28+5 | 4+0 |  |  | 32+5 |
| UX25 | A |  | 17+5 |  |  | 17+5 |
| UX25 | C | 9+0 | 25+6 |  |  | 34+6 |
| Subtotal in UX25 | All groups | 64+12 | 50+11 |  |  | 114+23 |
| PX24 | CR1 (DAQ) |  |  | 1+0 | 34+0 | 35+0 |
| PX24 | CR2 (HLT) |  |  | 1+0 | 39+0 | 40+0 |
| PX24 | CR3 (DCS + HLT) |  |  | 6+7 | 22+0 | 28+7 |
| PX24 | CR4 (HV + Misc.) |  |  | 32+2 |  | 32+2 |
| PX24 | CR5 (Safety) |  |  | 8+0 |  | 8+0 |
| Subtotal in PX24 | All CR’s |  |  | 48+9 | 95+0 | 143+9 |
| Misc. in SX2 | ACR |  |  | 2+0 |  | 2+0 |
| Misc. in PX24 | MCR |  |  | 5+0 |  | 5+0 |
| Misc. in US25 | / |  |  | 0+3 |  | 0+3 |
| Subtotal in Misc. |  |  |  | 7+3 |  | 7+3 |
| Total in ALICE |  | 64+12 | 50+11 | 55+12 | 95+0 | 264+35 |

Table 13: Number of electronic racks per type in ALICE

Figure 14:  Typical internal rack arrangement: a TPC-LV rack (in group A)

Each rack with vertical air ventilation will be equipped with a standard 4U rack ventilation and monitoring unit normally placed at the very top of the rack. This unit was developed for the LHC rack project. The principal tasks of the rack ventilation and monitoring unit are to ensure rack air flow by means of suitable turbines, and to supervise the thermal environment in the rack in order to provide optimum operating conditions. However, the high concentrations of power in each rack imply that the rack ventilation and monitoring unit is also a vital component for the overall safety of the experiment.  Additionally, it is planned to equip all racks with a thermal overload protection and a smoke detector.

The other 95 rack locations (in CR1-CR3) are planned to house commercial, rack-mounted PCs for which the air ventilation needs to be horizontal. The standard rack ventilation and monitoring unit not being suitable for those racks, a dedicated monitoring system is under investigation.

# Appendix 1:  List of Coordinators and Contact Persons

| Sub-detector/ Sub-system | Coordinator | Institute | Contact Person |
| --- | --- | --- | --- |
| ACORDE | A. Fernandez Tellez | U. Mexico | / |
| CPV | S. Sadovsky | Protvino | H. Müller |
| CTP | D. Evans | U. Birmingham / CERN | O. Villalobos-Baillie |
| DAQ | P. Vande Vyvre | PH-AID | / |
| DCS | L. Jirden | PH- AIT | A. Augustinus |
| EMC | T. Cormier | Wayne State U. | T. Awes |
| FMD | J.J. Gaardhoje | NBI Copenhagen | B. Nielsen |
| HLT | V. Lindenstruth | U. Heidelberg (KIP) | H. Tilsner |
| HMPID | P. Martinengo | PH-AIT | A. Tauro |
| MCH | H. Borel | IPN Orsay | / |
| MTR | A. Musso | INFN Torino | P. Dupieux |
| PHOS | V. Manko | Kurchatov | H. Müller |
| PMD | Y. Viyogi | Calcutta | M. Ganti |
| SDD | F. Tosello | INFN Torino | / |
| SPD | G. Stefanini | PH-AIT | A. Kluge |
| SSD | G. Nooren | NIKHEF | A. de Haas |
| TPC | P. Braun-Munzinger | GSI Darmstadt | R. Renfordt |
| TRD | J. Wessels | U. Heidelberg (HDP) | D. Emschermann |
| TOF | R. Nania | INFN Bologna | / |
| T0 | W.H. Trzaska | HIP, U. Jyväskylä (HIP) | T. Malkiewicz |
| V0 | J.Y. Grossiord | IPN Lyon | / |
| ZDC | M. Gallio | INFN Torino | / |

# Appendix 2:  Rack Allocation Detailed Listing

The following pages detail the rack allocation in each one of the four rack group (I, O, A, C) of the UX25 cavern, in each counting room (CR1-CR5) of the PX24 shaft, in ACR at ground level of SX2 building, in MCR at level 4 of PX24 (close to CR4) and in US25 underground area, giving for each rack location: rack type, name, usage (i.e. the sub-detector or sub-system the rack is related to) and, whenever this is known, function within that sub-detector or sub-system.

Group ‘I’

31+7=38

| Rack # | Rack type | Rack name | Detector-Function |
| --- | --- | --- | --- |
| I00 | LHC-41 | 1HMPU2YI00 | HMPID-TR |
| I01 | LHC-41 | 1HMPU2YI01 | HMPID-LV |
| I02 | LHC-41 | 1HMPU2YI02 | HMPID-LV |
| I03 | LHC-41 | 1TOFU2YI03 | TOF-LV |
| I04 | LHC-41 | 1TOFU2YI04 | TOF-LV |
| I05 | LHC-41 | 1TOFU2YI05 | TOF-LV |
| I06 | LHC-41 | 1TRDU2YI06 | TRD-LV |
| I07 | LHC-41 | 1TRDU2YI07 | TRD-HV |
| I08 | LHC-41 | 1TRDU2YI08 | TRD-CO |
| I09 | LHC-41 | NA | Spare location |
| I10 | LHC-41 | NA | Spare location |
| I11 | LHC-41 | NA | Spare location |
| I12 | LHC-41 | NA | Spare location |
| I13 | LHC-41 | NA | Spare location |
| I14 | LHC-41 | NA | Spare location |
| I15 | LHC-41 | NA | Spare location |
| I16 | LHC-41 | 1INTU2YI16 | TS-EL |
| I17 | LHC-41 | 1INTU2YI17 | TS-EL |
| I18 | LHC-41 | 1SPDU2YI18 | SPD-LV |
| I19 | LHC-41 | 1SPDU2YI19 | SPD-LV |
| I20 | LHC-41 | 1V00U2YI20 | V0-RO |
| I21 | LHC-41 | 1SSDU2YI21 | SSD-CO |
| I22 | LHC-41 | 1SSDU2YI22 | SSD-LV/HV |
| I23 | LHC-41 | 1SSDU2YI23 | SSD-LV/HV |
| I24 | LHC-41 | 1SSDU2YI24 | SSD-RO |
| I25 | LHC-41 | 1TPCU2YI25 | TPC-LV |
| I26 | LHC-41 | 1TRDU2YI26 | TRD-LV |
| I27 | LHC-41 | 1TRDU2YI27 | TRD-LV |
| I28 | LHC-41 | 1TRDU2YI28 | TRD-LV |
| I29 | LHC-41 | 1TRDU2YI29 | TRD-LV |
| I30 | LHC-41 | 1TOFU2YI30 | TOF-LV |
| I31 | LHC-41 | 1TOFU2YI31 | TOF-LV |
| I32 | LHC-41 | 1TOFU2YI32 | TOF-LV |
| I33 | LHC-41 | 1TOFU2YI33 | Spare rack for TOF |
| I34 | LHC-52 | 1MTRU2YI34 | MTR-RO |
| I35 | LHC-52 | 1MTRU2YI35 | MTR-RO |
| I36 | LHC-52 | 1MTRU2YI36 | MTR-RO |
| I37 | LHC-52 | 1MTRU2YI37 | MTR-RO |

Group ‘O’

32+5(+1)=37(+1)

| Rack # | Rack type | Rack name | Detector-Function |
| --- | --- | --- | --- |
| O00 | LHC-41 | NA | Spare location |
| O01 | LHC-41 | NA | Spare location |
| O02 | LHC-41 | 1TOFU2YO02 | Spare rack for TOF |
| O03 | LHC-41 | 1TOFU2YO03 | TOF-LV |
| O04 | LHC-41 | 1TOFU2YO04 | TOF-LV |
| O05 | LHC-41 | 1TOFU2YO05 | TOF-LV |
| O06 | LHC-41 | 1TRDU2YO06 | TRD-LV |
| O07 | LHC-41 | 1TRDU2YO07 | TRD-HV |
| O08 | LHC-41 | 1TRDU2YO08 | TRD-CO |
| O09 | LHC-41 | NA | Spare location |
| O10 | LHC-41 | NA | Spare location |
| O11 | LHC-41 | NA | Spare location |
| O12 | LHC-41 | 1EMCU2YO12 | EMC-LV |
| O13 | LHC-41 | 1FMDU2YO13 | FMD-LV |
| O14 | LHC-41 | 1ACOU2YO14 | ACORDE-LV |
| O15 | LHC-41 | 1ACOU2YO15 | ACORDE-RO |
| O16 | LHC-41 | 1INTU2YO16 | TS-EL |
| O17 | (Special gas rack) | (NA) | (TPC-GAS) |
| O18 | LHC-41 | 1T00U2YO18 | T0-LV/RO |
| O19 | LHC-41 | 1T00U2YO19 | T0-RO |
| O20 | LHC-41 | 1SDDU2YO20 | SDD-LV |
| O21 | LHC-41 | 1INTU2YO21 | Sniffer Detection |
| O22 | LHC-41 | 1INTU2YO22 | Sniffer Detection |
| O23 | LHC-41 | 1INTU2YO23 | Spare rack for Sniffers |
| O24 | LHC-41 | NA | Min-equipped spare rack |
| O25 | LHC-41 | 1TPCU2YO25 | TPC-LV |
| O26 | LHC-41 | 1TRDU2YO26 | TRD-LV |
| O27 | LHC-41 | 1TRDU2YO27 | TRD-LV |
| O28 | LHC-41 | 1TRDU2YO28 | TRD-LV |
| O29 | LHC-41 | 1TRDU2YO29 | TRD-LV |
| O30 | LHC-41 | 1TOFU2YO30 | TOF-LV |
| O31 | LHC-41 | 1TOFU2YO31 | TOF-LV |
| O32 | LHC-41 | 1TOFU2YO32 | TOF-LV |
| O33 | LHC-41 | 1TOFU2YO33 | Spare rack for TOF |
| O34 | LHC-52 | 1MTRU2YO34 | MTR-RO |
| O35 | LHC-52 | 1MTRU2YO35 | MTR-RO |
| O36 | LHC-52 | 1MTRU2YO36 | MTR-RO |
| O37 | LHC-52 | 1MTRU2YO37 | MTR-RO |

Group ‘A’

17+5=22

| Rack # | Rack type | Rack name | Detector-Function |
| --- | --- | --- | --- |
| A00 | LHC-52 | NA | Spare location |
| A01 | LHC-52 | NA | Spare location |
| A02 | LHC-52 | NA | Spare location |
| A03 | LHC-52 | 1INTU2YA03 | Vacuum |
| A04 | LHC-52 | 1PMDU2YA04 | TPC-LV |
| A05 | LHC-52 | 1PMDU2YA05 | TPC-LV |
| A06 | LHC-52 | 1TPCU2YA06 | TPC-CP |
| A07 | LHC-52 | 1TPCU2YA07 | TPC-GP |
| A08 | LHC-52 | 1TPCU2YA08 | PMD-LV |
| A09 | LHC-52 | 1TPCU2YA09 | PMD-LV |
| A10 | LHC-52 | NA | Spare location |
| A11 | LHC-52 | NA | Spare location |
| A12 | LHC-52 | 1SDDU2YA12 | SDD-LV |
| A13 | LHC-52 | NA | Min-equipped spare rack |
| A14 | LHC-52 | 1SPDU2YA14 | SPD-LV |
| A15 | LHC-52 | 1SPDU2YA15 | SPD-LV |
| A16 | LHC-52 | 1CPVU2YA16 | CPV-LV |
| A17 | LHC-52 | 1PHSU2YA17 | PHS-LV |
| A18 | LHC-52 | 1INTU2YA18 | TS-EL |
| A19 | LHC-52 | 1SSDU2YA19 | SSD-RO |
| A20 | LHC-52 | 1SSDU2YA20 | SSD-LV/HV |
| A21 | LHC-52 | 1SSDU2YA21 | SSD-LV/HV |

Group ‘C’

34+6=40

| Rack # | Rack type | Rack name | Detector-Function |
| --- | --- | --- | --- |
| C00 | LHC-52 | 1INTU2YC00 | TS-EL |
| C01 | LHC-52 | 1MTRU2YC01 | MTR-LV |
| C02 | LHC-52 | 1TOFU2YC02 | TOF-RO |
| C03 | LHC-52 | 1TOFU2YC03 | TOF-TR |
| C04 | LHC-52 | 1SPDU2YC04 | SPD-TR |
| C05 | LHC-52 | 1MCHU2YC05 | MCH-spare |
| C06 | LHC-52 | NA | Spare location |
| C07 | LHC-52 | NA | Spare location |
| C08 | LHC-52 | 1MCHU2YC08 | MCH-LV |
| C09 | LHC-52 | 1MCHU2YC09 | MCH-LV |
| C10 | LHC-52 | 1MCHU2YC10 | MCH-LV |
| C11 | LHC-52 | 1MCHU2YC11 | MCH-LV |
| C12 | LHC-52 | NA | Min-equipped spare rack |
| C13 | LHC-52 | NA | Min-equipped spare rack |
| C14 | LHC-52 | 1TPCU2YC14 | TPC-CP |
| C15 | LHC-52 | 1TPCU2YC15 | TPC-GP |
| C16 | LHC-41 | 1TRDU2YC16 | TRD-CT |
| C17 | LHC-52 | 1TRDU2YC17 | TRD-CT |
| C18 | LHC-52 | 1TRDU2YC18 | TRD-CT |
| C19 | LHC-41 | NA | Unequipped spare rack |
| C20 | LHC-41 | 1TRIU2YC20 | TRI-CTP |
| C21 | LHC-41 | 1TRIU2YC21 | TRI-CTP |
| C22 | LHC-41 | 1XXXU2YC22 | Multiple Trigger |
| C23 | LHC-41 | 1XXXU2YC23 | Multiple Trigger |
| C24 | LHC-41 | 1TRIU2YC24 | TRI-CTP |
| C25 | LHC-41 | 1TRIU2YC25 | TRI-CTP |
| C26 | LHC-41 | 1TRIU2YC26 | TRI-CTP |
| C27 | LHC-41 | 1TRIU2YC27 | TRI-CTP |
| C28 | LHC-52 | 1INTU2YC28 | BIC (Beam Interlock Controller) |
| C29 | LHC-52 | 1INTU2YC29 | BIC (Beam Interlock Controller) |
| C30 | LHC-52 | 1INTU2YC30 | Vacuum |
| C31 | LHC-52 | 1MTRU2YC31 | MTR-LV |
| C32 | LHC-52 | 1MCHU2YC32 | MCH-spare |
| C33 | LHC-52 | NA | Spare location |
| C34 | LHC-52 | NA | Spare location |
| C35 | LHC-52 | NA | Spare location |
| C36 | LHC-52 | 1MCHU2YC36 | MCH-LV |
| C37 | LHC-52 | 1MCHU2YC37 | MCH-LV |
| C38 | LHC-52 | 1MCHU2YC38 | MCH-LV |
| C39 | LHC-52 | 1MCHU2YC39 | MCH-LV |

CR1

35+0=35

| Rack # | Rack type | Rack name | Detector-Function |
| --- | --- | --- | --- |
| CR1-X01 | LEP-56 | 1INTC1YX01 | TS-EL |
| CR1-X02 | LEP-56PC | 1DAQC1YX02 | DAQ-LDCs (HLT) |
| CR1-X03 | LEP-56PC | 1DAQC1YX03 | DAQ-LDCs (MCH-MTR) |
| CR1-X04 | LEP-56PC | 1DAQC1YX04 | DAQ-LDCs (PHOS-CPV) |
| CR1-X05 | LEP-56PC | 1DAQC1YX05 | DAQ-LDCs (HMPID-PMD) |
| CR1-X06 | LEP-56PC | 1DAQC1YX06 | DAQ-LDCs (TOF) |
| CR1-X07 | LEP-56PC | 1DAQC1YX07 | DAQ-LDCs (TOF) |
| CR1-X08 | LEP-56PC | 1DAQC1YX08 | DAQ-LDCs (TRD) |
| CR1-X09 | LEP-56PC | 1DAQC1YX09 | DAQ-LDCs (SSD-FMD) |
| CR1-X10 | LEP-56PC | 1DAQC1YX10 | DAQ-LDCs (SDD-ZDC-ACORDE) |
| CR1-X11 | LEP-56PC | 1DAQC1YX11 | DAQ-LDCs (SPD) |
| CR1-Y01 | LEP-56PC | 1DAQC1YY01 | DAQ-LDCs (TPC) |
| CR1-Y02 | LEP-56PC | 1DAQC1YY02 | DAQ-LDCs (TPC) |
| CR1-Y03 | LEP-56PC | 1DAQC1YY03 | DAQ-LDCs (TPC) |
| CR1-Y04 | LEP-56PC | 1DAQC1YY04 | DAQ-LDCs (TPC) |
| CR1-Y05 | LEP-56PC | 1DAQC1YY05 | DAQ-LDCs (TPC) |
| CR1-Y06 | LEP-56PC | 1DAQC1YY06 | DAQ-LDCs (TPC) |
| CR1-Y07 | LEP-56PC | 1DAQC1YY07 | DAQ-LDCs (TPC) |
| CR1-Y08 | LEP-56PC | 1DAQC1YY08 | DAQ-LDCs (TPC) |
| CR1-Y09 | LEP-56PC | 1DAQC1YY09 | DAQ-LDCs (TPC) |
| CR1-Y10 | LEP-56PC | 1DAQC1YY10 | DAQ-LDCs (TPC) |
| CR1-Y11 | LEP-56PC | 1DAQC1YY11 | DAQ-LDCs (TPC) |
| CR1-Y12 | LEP-56PC | 1DAQC1YY12 | DAQ-LDCs (TPC) |
| CR1-Y13 | LEP-56PC | 1DAQC1YY13 | DAQ-LDCs (EMC) |
| CR1-Y14 | LEP-56PC | 1DAQC1YY14 | Spare rack for DAQ |
| CR1-Z01 | LEP-56PC | 1DAQC1YZ01 | DAQ-CO (Test & Comm.) |
| CR1-Z02 | LEP-56PC | 1DAQC1YZ02 | DAQ-CO (Servers) |
| CR1-Z03 | LEP-56PC | 1DAQC1YZ03 | DAQ-GDCs |
| CR1-Z04 | LEP-56PC | 1DAQC1YZ04 | DAQ-GDCs |
| CR1-Z05 | LEP-56PC | 1DAQC1YZ05 | DAQ-CO (EB SW& KVM) |
| CR1-Z06 | LEP-56PC | 1DAQC1YZ06 | DAQ-GDCs |
| CR1-Z07 | LEP-56PC | 1DAQC1YZ07 | DAQ-GDCs |
| CR1-Z08 | LEP-56PC | 1DAQC1YZ08 | DAQ-GDCs |
| CR1-Z09 | LEP-56PC | 1DAQC1YZ09 | Spare rack for DAQ |
| CR1-Z10 | LEP-56PC | 1DAQC1YZ10 | Spare rack for DAQ |

CR2

40+0=40

| Rack # | Rack type | Rack name | Detector-Function |
| --- | --- | --- | --- |
| CR2-X01 | LEP-56 | 1INTC2YX01 | TS-EL |
| CR2-X02 | LEP-56PC | 1HLTC2YX02 | HLT-CO (NSM) |
| CR2-X03 | LEP-56PC | 1HLTC2YX03 | HLT-PC |
| CR2-X04 | LEP-56PC | 1HLTC2YX04 | HLT-PC |
| CR2-X05 | LEP-56PC | 1HLTC2YX05 | HLT-PC |
| CR2-X06 | LEP-56PC | 1HLTC2YX06 | HLT-PC |
| CR2-X07 | LEP-56PC | 1HLTC2YX07 | HLT-PC |
| CR2-X08 | LEP-56PC | 1HLTC2YX08 | HLT-PC |
| CR2-X09 | LEP-56PC | 1HLTC2YX09 | HLT-PC |
| CR2-X10 | LEP-56PC | 1HLTC2YX10 | HLT-PC |
| CR2-Y01 | LEP-56PC | 1HLTC2YY01 | HLT-CO (NSM) |
| CR2-Y02 | LEP-56PC | 1HLTC2YY02 | HLT-PC |
| CR2-Y03 | LEP-56PC | 1HLTC2YY03 | HLT-PC |
| CR2-Y04 | LEP-56PC | 1HLTC2YY04 | HLT-PC |
| CR2-Y05 | LEP-56PC | 1HLTC2YY05 | HLT-PC |
| CR2-Y06 | LEP-56PC | 1HLTC2YY06 | HLT-PC |
| CR2-Y07 | LEP-56PC | 1HLTC2YY07 | HLT-PC |
| CR2-Y08 | LEP-56PC | 1HLTC2YY08 | HLT-PC |
| CR2-Y09 | LEP-56PC | 1HLTC2YY09 | HLT-PC |
| CR2-Y10 | LEP-56PC | 1HLTC2YY10 | HLT-PC |
| CR2-Y11 | LEP-56PC | 1HLTC2YY11 | HLT-PC |
| CR2-Y12 | LEP-56PC | 1HLTC2YY12 | HLT-PC |
| CR2-Y13 | LEP-56PC | 1HLTC2YY13 | HLT-PC |
| CR2-Y14 | LEP-56PC | 1HLTC2YY14 | HLT-PC |
| CR2-Y15 | LEP-56PC | 1HLTC2YY15 | HLT-PC |
| CR2-Y16 | LEP-56PC | 1HLTC2YY16 | HLT-PC |
| CR2-Y17 | LEP-56PC | 1HLTC2YY17 | HLT-PC |
| CR2-Z01 | LEP-56PC | 1HLTC2YZ01 | HLT-CO (NSM) |
| CR2-Z02 | LEP-56PC | 1HLTC2YZ02 | HLT-PC |
| CR2-ZO3 | LEP-56PC | 1HLTC2YZ03 | HLT-PC |
| CR2-Z04 | LEP-56PC | 1HLTC2YZ04 | HLT-PC |
| CR2-Z05 | LEP-56PC | 1HLTC2YZ05 | HLT-PC |
| CR2-Z06 | LEP-56PC | 1HLTC2YZ06 | HLT-PC |
| CR2-Z07 | LEP-56PC | 1HLTC2YZ07 | HLT-PC |
| CR2-Z08 | LEP-56PC | 1HLTC2YZ08 | HLT-PC |
| CR2-Z09 | LEP-56PC | 1HLTC2YZ09 | HLT-PC |
| CR2-Z10 | LEP-56PC | 1HLTC2YZ10 | HLT-PC |
| CR2-Z11 | LEP-56PC | 1HLTC2YZ11 | HLT-PC |
| CR2-Z12 | LEP-56PC | 1HLTC2YZ12 | HLT-PC |
| CR2-Z13 | LEP-56PC | 1HLTC2YZ13 | HLT-PC |

CR3

28+7=35

| Rack # | Rack type | Rack name | Detector-Function |
| --- | --- | --- | --- |
| CR3-X01 | LEP-56PC | 1HLTC3YX01 | HLT-PC |
| CR3-X02 | LEP-56PC | 1HLTC3YX02 | HLT-PC |
| CR3-X03 | LEP-56PC | 1HLTC3YX03 | HLT-PC |
| CR3-X04 | LEP-56PC | 1HLTC3YX04 | HLT-PC |
| CR3-X05 | LEP-56PC | 1HLTC3YX05 | HLT-PC |
| CR3-X06 | LEP-56PC | 1HLTC3YX06 | HLT-PC |
| CR3-X07 | LEP-56PC | 1HLTC3YX07 | HLT-PC |
| CR3-X08 | LEP-56PC | 1HLTC3YX08 | HLT-PC |
| CR3-X09 | LEP-56PC | 1HLTC3YX09 | HLT-PC |
| CR3-X10 | LEP-56PC | 1HLTC3YX10 | HLT-PC |
| CR3-X11 | LEP-56PC | 1HLTC3YX11 | HLT-PC |
| CR3-X12 | LEP-56PC | 1HLTC3YX12 | HLT-PC |
| CR3-Y01 | LEP-56 | 1INTC3YY01 | TS-EL |
| CR3-Y02 | LEP-56PC | 1TOFC3YY02 | TOF-CO |
| CR3-Y03 | LEP-56PC | 1TOFC3YY03 | TOF-CO |
| CR3-Y04 | LEP-56PC | 1TOFC3YY04 | TOF-CO |
| CR3-Y05 | LEP-56 | NA | Min-equipped spare rack |
| CR3-Y06 | LEP-56 | NA | Min-equipped spare rack |
| CR3-Y07 | LEP-56 | NA | Min-equipped spare rack |
| CR3-Y08 | LEP-56 | NA | Min-equipped spare rack |
| CR3-Y09 | LEP-56 | NA | Unequipped spare rack |
| CR3-Y10 | LEP-56 | NA | Unequipped spare rack |
| CR3-Y11 | LEP-56 | NA | Unequipped spare rack |
| CR3-Y12 | LEP-56 | NA | Unequipped spare rack |
| CR3-Y13 | LEP-56 | NA | Unequipped spare rack |
| CR3-Z01 | LEP-56PC | 1DCSC3YZ01 | DCS-DC (ITS, FMD) |
| CR3-Z02 | LEP-56PC | 1DCSC3YZ02 | DCS-DC (TPC,HMP,PMD) |
| CR3-Z03 | LEP-56PC | 1DCSC3YZ03 | DCS-DC (TRD,V0,T0) |
| CR3-Z04 | LEP-56PC | 1DCSC3YZ04 | DCS-DC (PHS,CPV,EMC,ZDC,ACO) |
| CR3-Z05 | LEP-56PC | 1DCSC3YZ05 | DCS-CO (MCH,MTR,TOF) |
| CR3-Z06 | LEP-56PC | 1DCSC3YZ06 | DCS TRG,SPD TRG, DCS |
| CR3-Z07 | LEP-56PC | 1DCSC3YZ07 | DCS Central DCS |
| CR3-Z08 | LEP-56 | 1DCSC3YZ08 | DCS-CO (Fieldbusses) |
| CR3-Z09 | LEP-56 | NA | Unequipped spare rack |
| CR3-Z10 | LEP-56 | NA | Unequipped spare rack |

CR4

32+2=34

| Rack # | Rack type | Rack name | Detector-Function |
| --- | --- | --- | --- |
| CR4-X01 | LEP-56 | 1MCHC4YX01 | MCH-GMS |
| CR4-X02 | LEP-56 | 1ACOC4YX02 | ACORDE-HV |
| CR4-X03 | LEP-56 | 1PMDC4YX03 | PMD-HV |
| CR4-X04 | LEP-56 | 1ZDCC4YX04 | ZDC-RO |
| CR4-X05 | LEP-56 | 1ZDCC4YX05 | ZDC-RO |
| CR4-X06 | LEP-56 | 1FMDC4YX06 | FMD-HV |
| CR4-X07 | LEP-56 | NA | Min-equipped spare rack |
| CR4-X08 | LEP-56 | NA | Min-equipped spare rack |
| CR4-X09 | LEP-56 | NA | Min-equipped spare rack |
| CR4-X10 | LEP-56 | NA | Unequipped spare rack |
| CR4-X11 | LEP-56 | NA | Unequipped spare rack |
| CR4-Y01 | LEP-56 | 1SPDC4YY01 | SPD-RO |
| CR4-Y02 | LEP-56 | 1SPDC4YY02 | SPD-RO |
| CR4-Y03 | LEP-56 | 1SPDC4YY03 | SPD-HV |
| CR4-Y04 | LEP-56 | 1SDDC4YY04 | SDD-HV |
| CR4-Y05 | LEP-56 | 1SDDC4YY05 | SDD-RO |
| CR4-Y06 | LEP-56 | 1SSDC4YY06 | SSD-HV |
| CR4-Y07 | LEP-56 | NA | Min-equipped spare rack |
| CR4-Y08 | LEP-56 | 1TPCC4YY08 | TPC-HV |
| CR4-Y09 | LEP-56 | NA | Min-equipped spare rack |
| CR4-Y10 | LEP-56 | 1XXXC4YY10 | PHOS/CPV/EMC-HV |
| CR4-Y11 | LEP-56 | 1HMPC4YY11 | HMPID-HV |
| CR4-Y12 | LEP-56 | 1TRDC4YY12 | TRD-HV |
| CR4-Y13 | LEP-56 | 1TRDC4YY13 | TRD-HV |
| CR4-Y14 | LEP-56 | NA | Min-equipped spare rack |
| CR4-Z01 | LEP-56 | 1INTC4YZ01 | TS-EL |
| CR4-Z02 | LEP-56 | 1TOFC4YZ02 | TOF-HV |
| CR4-Z03 | LEP-56 | 1TOFC4YZ03 | TOF-HV |
| CR4-Z04 | LEP-56 | 1XXXC4YZ04 | T0/V0-HV |
| CR4-Z05 | LEP-56 | 1MCHC4YZ05 | MCH-HV |
| CR4-Z06 | LEP-56 | 1MTRC4YZ06 | MTR-HV |
| CR4-Z07 | LEP-56 | NA | Min-equipped spare rack |
| CR4-Z08 | LEP-56 | 1TPCC4YZ08 | TPC-VHV |
| CR4-Z09 | LEP-56 | 1DCSC4YZ09 | DCS-DSS |

CR5

8+0=8

| Rack # | Rack type | Rack name | Detector-Function |
| --- | --- | --- | --- |
| CR5-X01 | LEP-56 | 1INTC5YX01 | Sniffer Control |
| CR5-X02 | LEP-56 | 1INTC5YX02 | Fire Detection (racks) (cavern) |
| CR5-X03 | LEP-56 | 1INTC5YX03 | Fire Detection (racks) |
| CR5-X04 | LEP-56 | 1INTC5YX04 | Fire Detection (detector) |
| CR5-X05 | LEP-56 | 1INTC5YX05 | Radio-protection |
| CR5-X06 | LEP-56 | 1INTC5YX06 | Spare rack for Safety |
| CR5-X07 | LEP-56 | 1HMPC5YX07 | HMPID-CO |
| CR5-X08 | LEP-56 | 1HMPC5YX08 | HMPID-CO |

ACR

2+0=2

| Rack # | Rack type | Rack name | Detector-Function |
| --- | --- | --- | --- |
| SX2-X01 | LEP-56 | 1DCSSXYX01 | DCS-DSS |
| SX2-X02 | LEP-56 | 1TRISXYX02 | TRI |

MCR

5+0=5

| Rack # | Rack type | Rack name | Detector-Function |
| --- | --- | --- | --- |
| CR4-M01 | LEP-56 | 1INTC4YM01 | Magnets Control |
| CR4-M02 | LEP-56 | 1INTC4YM02 | Magnets Control |
| CR4-M03 | LEP-56 | 1INTC4YM03 | Magnets Control |
| CR4-M04 | LEP-56 | 1INTC4YM04 | Magnets Control |
| CR4-M05 | LEP-56 | 1INTC4YM05 | Magnets Control |

US25

0+3=3

| Rack # | Rack type | Rack name | Detector-Function |
| --- | --- | --- | --- |
| US2-X01 | LEP-56 | NA | Unequipped spare rack |
| US2-X02 | LEP-56 | NA | Unequipped spare rack |
| US2-X03 | LEP-56 | NA | Unequipped spare rack |

”Integration  Racks”

(27)

There are 27 miscellaneous electronic racks which are not related to any particular sub-detector or sub-system, but are of general interest to the experiment. Although they have already been included in the previous listings, they are also regrouped  here for convenience.

| Rack # | Rack type | Rack name | Detector-Function |
| --- | --- | --- | --- |
| I16 | LHC-41 | 1INTU2YI16 | TS-EL |
| I17 | LHC-41 | 1INTU2YI17 | TS-EL |
| O16 | LHC-41 | 1INTU2YO16 | TS-EL |
| O21 | LHC-41 | 1INTU2YO21 | Sniffer Detection |
| O22 | LHC-41 | 1INTU2YO22 | Sniffer Detection |
| O23 | LHC-41 | 1INTU2YO23 | Spare rack for Sniffers |
| A03 | LHC-52 | 1INTU2YA03 | Vacuum |
| A18 | LHC-52 | 1INTU2YA18 | TS-EL |
| C00 | LHC-52 | 1INTU2YC00 | TS-EL |
| C28 | LHC-52 | 1INTU2YC28 | BIC (Beam Interlock Controller) |
| C29 | LHC-52 | 1INTU2YC29 | BIC (Beam Interlock Controller) |
| C30 | LHC-52 | 1INTU2YC30 | Vacuum |
| CR1-X01 | LEP-56 | 1INTC1YX01 | TS-EL |
| CR2-X01 | LEP-56 | 1INTC2YX01 | TS-EL |
| CR3-Y01 | LEP-56 | 1INTC3YY01 | TS-EL |
| CR4-Z01 | LEP-56 | 1INTC4YZ01 | TS-EL |
| CR4-M01 | LEP-56 | 1INTC4YM01 | Magnets Control |
| CR4-M02 | LEP-56 | 1INTC4YM02 | Magnets Control |
| CR4-M03 | LEP-56 | 1INTC4YM03 | Magnets Control |
| CR4-M04 | LEP-56 | 1INTC4YM04 | Magnets Control |
| CR4-M05 | LEP-56 | 1INTC4YM05 | Magnets Control |
| CR5-X01 | LEP-56 | 1INTC5YX01 | Sniffer Control |
| CR5-X02 | LEP-56 | 1INTC5YX02 | Fire Detection (racks) |
| CR5-X03 | LEP-56 | 1INTC5YX03 | Fire Detection (racks) |
| CR5-X04 | LEP-56 | 1INTC5YX04 | Fire Detection (detector) |
| CR5-X05 | LEP-56 | 1INTC5YX05 | Radio-protection |
| CR5-X06 | LEP-56 | 1INTC5YX06 | Spare rack for Safety |

# Footnotes

LHC rack:  http://ess.web.cern.ch/ESS/racks/index.htm

Common project in progress,  http://alicedcs.web.cern.ch/AliceDCS/pcrackcool/

The rack name conforms to the naming conventions described in EDMS No 696434 document.

# Text boxes

O

C

I

A